## Slide 1
INITIAL DRAFT • CONTENT REVIEW
Mesh realization is part of the result
Repeatability of individualized temporal-interference E-field simulations
Boyan Ivanov • Lab Journal Club • 25 September 2026
Fresh remeshing produces percent-level spread; repeated solving on one mesh is nearly deterministic.
FULLY NESTED CHECK
40
independent meshes
×
40
solves per mesh
3,200 simulation records across cohort + nested experiments
Notes: Opening (about 40 seconds): Individualized TI simulations are usually spoken about as though one anatomy and one montage produce one field map. This experiment asks whether that output is actually unique when the tetrahedral mesh is regenerated. The answer is no: in this workflow, the mesh realization contributes percent-level uncertainty.
Preview the two experiments: a ten-participant remesh-versus-fixed comparison and one fully nested 40-by-40 case that separates between-mesh from within-mesh variation.

## Slide 2
TAKE-HOME FIRST
The field estimate is mesh-dependent
TI repeatability • journal club
02
1.81–3.65%
Left-hippocampus CV across remesh repeats
1.62–2.79%
Right-M1 CV across remesh repeats
95.7%
Hippocampal draws with ≥1 rank reversal
99.9996%
Variance share attributed to mesh in one nested subject
Central conclusion
Within the evaluated CHARM–SimNIBS workflow, mesh generation—not repeated solution on a fixed mesh—dominates repeated-run variability.
Interpretation boundary
The 40×40 variance decomposition is a single-participant sensitivity analysis. It strengthens source attribution, but it is not a population variance estimate.
Corrected spherical-ROI analysis freeze: 11 Sep 2026
Notes: The cohort analysis shows remesh CVs of 1.81–3.65% in left hippocampus and 1.62–2.79% in right M1. A single remesh repeat often changes at least one pairwise subject ordering. In the fully nested subject, 99.9996% of observed variance is assigned to differences between meshes.
Emphasize the boundary: the nested percentage is conditional on one subject, one target, and this workflow. It is not a claim that all simulation uncertainty everywhere is mesh-driven.

## Slide 3
WHY THIS MATTERS
Identical inputs still pass through a variable numerical representation
TI repeatability • journal club
03
1
MRI + labels
fixed anatomy
2
CHARM mesh
regenerate or reuse
3
FEM fields
two carrier fields
4
TI envelope
max-TI combination
5
Spherical ROI
median field
experimental factor
Held constant
anatomy • tissue labels • electrodes • currents • conductivities • software settings • ROI definition
Question: can a new valid tetrahedralization change a conclusion even when every scientific input is unchanged?
Context: Windhoff et al., 2013; Saturnino et al., 2019; Puonti et al., 2020
Notes: Walk left to right. The anatomy, labels, montage, currents, conductivities, software, and ROI stay fixed. The experimental factor is whether CHARM creates a fresh tetrahedral mesh or the same mesh workspace is reused.
The study is not comparing two biological states. It is measuring numerical repeatability of the modelling pipeline.

## Slide 4
STUDY DESIGN
Two complementary experiments separate pattern from source
TI repeatability • journal club
04
COHORT CONTRAST
Does the effect recur across people and targets?
10
participants
2
targets
40+40
runs / subject–target
Left hippocampus + right M1
5 female / 5 male • ages 26.00–79.17 years
1,600 simulations
FULLY NESTED
Which stage contributes the variance?
1
participant
40
independent meshes
40
solves / mesh
CC320616 • left hippocampus
Participant selected once with a fixed seed
1,600 simulations
3,200 completed simulation records in the presentation evidence base
CamCAN cohort; corrected spherical-fixed + nested analysis
Notes: The cohort contrast asks whether remesh-versus-fixed behavior is consistent across ten participants and both a deep and superficial target. The fully nested experiment asks where variation enters by crossing 40 independently generated meshes with 40 repeated solutions per mesh.
Do not combine the two sample sizes as though 3,200 were independent biological observations. These are technical simulation records.

## Slide 5
METHODS THAT AFFECT INTERPRETATION
The contrast changes one thing: the mesh realization
TI repeatability • journal club
05
REMESH
Fresh mesh generated for every repeat
Variation represented
mesh generation + FEM solution + export / ROI extraction
FIXED MESH
One mesh reused for every repeat
Variation represented
residual FEM solution + export / ROI extraction conditional on one mesh
PRIMARY OUTCOME
Median maximum-TI envelope
within the optimizer-matched, parcel-clipped spherical ROI
200 mm³ hippocampus
100 mm³ M1
Analysis
Per-participant SD/CV
•
20,000 single-repeat rank draws
•
balanced one-way random-effects decomposition
Participant is the population unit; repeats quantify computational variation.
Corrected selector aligned with the spherical analysis ROI
Notes: The remesh arm includes everything that can vary after the fixed inputs, including tetrahedralization. The fixed arm measures only residual solution and post-processing variation conditional on one selected mesh.
The fixed mesh is the remesh geometry nearest the median spherical-ROI result for that participant and target. This deliberately makes it representative of the remesh distribution; it does not make it the most anatomically accurate mesh.
Mention the correction only if useful here: the current fixed arm was rebuilt after aligning mesh selection with the optimizer-matched spherical ROI.

## Slide 6
RESULT 1 • LEFT HIPPOCAMPUS
Hippocampal fields vary by 1.81–3.65% under remeshing
TI repeatability • journal club
06
2.40%
median remesh CV
≥99.19%
minimum reduction in SD with fixed mesh
≤0.016%
maximum fixed-mesh CV
Blue spread collapses to an almost single orange value for every participant.
n=10; 40 remesh + 40 fixed-mesh repeats per participant
Notes: Read the plot as within-participant technical variability, not between-person uncertainty. Each pale blue cloud is 40 independently remeshed simulations. The orange fixed-mesh repeats are visually collapsed.
The corrected spherical-ROI remesh CV range is 1.81–3.65%, with a median of 2.40%. The smallest participant-level SD reduction after mesh reuse is 99.19%.

## Slide 7
RESULT 2 • RIGHT M1
M1 shows the same pattern: 1.62–2.79% remesh CV
TI repeatability • journal club
07
2.54%
median remesh CV
≥99.78%
minimum reduction in SD with fixed mesh
≤0.0053%
maximum fixed-mesh CV
Replication in a superficial target argues against a hippocampus-only artifact.
n=10; 40 remesh + 40 fixed-mesh repeats per participant
Notes: The right-M1 result is qualitatively the same. Corrected spherical-ROI remesh CVs range from 1.62% to 2.79%, median 2.54%. The fixed-mesh SD reduction is at least 99.78%.
This replication supports robustness across the two evaluated targets, but not universal generalization to all montages, meshing tools, or ROIs.

## Slide 8
RESULT 3 • RANKING UNCERTAINTY
Percent-level spread matters when subjects are closely matched
TI repeatability • journal club
08
LEFT HIPPOCAMPUS
95.7%
of 20,000 draws contained ≥1 reversed pair
0.867
median Kendall agreement
47.9%
largest exact pair reversal
Closest high-risk pair: CC121144 vs CC720941
RIGHT M1
88.5%
of 20,000 draws contained ≥1 reversed pair
0.911
median Kendall agreement
44.7%
largest exact pair reversal
Closest high-risk pair: CC610631 vs CC310407
Global ordering remains fairly concordant, but a one-mesh ranking is fragile near ties.
One remesh repeat selected independently for each participant per draw
Notes: The reference ordering uses each participant's 40-repeat mean. In each of 20,000 draws, one repeat is selected independently per participant.
At least one pair reverses in 95.7% of hippocampal draws and 88.5% of M1 draws. Median agreement remains high, so the message is not that all rankings are random. It is that close pairs are sensitive to which valid mesh was selected.
These are uncertainty measures, not p-values.

## Slide 9
MECHANISTIC EVIDENCE
Remeshing changes the numerical head model—not only the final scalar
TI repeatability • journal club
09
Example: CC320616, left-hippocampus remesh arm
7,369
mean within-participant SD of total tetrahedral element count • hippocampus
7,704
mean within-participant SD of total tetrahedral element count • M1
Interpret carefully
Element count and tissue fractions confirm different realizations; they do not identify the causal boundary change.
Tissue deviations are percentage points from each tissue's 40-repeat mean
Notes: The heatmap shows small but structured shifts in the proportion of volume assigned to tissue classes across remesh realizations. Total tetrahedral element count also varies substantially within participant, while it is constant when the mesh is reused.
Do not claim that a particular tissue transition caused the field changes. Element count is coarse, and local boundaries, element quality, electrode–skin geometry, and interpolation can also matter.

## Slide 10
NESTED DESIGN
The nested design creates two separable levels of technical variation
TI repeatability • journal club
10
40 independent meshes
each reused for 40 complete solutions
mesh 01
…
mesh 02
…
mesh 03
…
mesh 04
…
mesh 05
…
⋮
40 repeats conditional on the same geometry
One fixed participant and target • 40 independently generated meshes • 40 complete solutions per mesh
BALANCED
40 meshes × 40 solutions
Every mesh contributes the same number of observations and therefore has equal weight.
NESTED
Each solution belongs to one mesh
Within-mesh comparisons hold the geometry fixed; mesh means are compared across geometries.
RANDOM MESH EFFECT
Meshes are sampled realizations
The goal is to estimate pipeline variability—not to compare named meshes as conditions.
Two questions: how far apart are mesh means, and how tightly do repeats cluster within a mesh?
Notes: The hierarchy matters before the equation. The design is balanced because all 40 meshes have 40 solutions. It is nested because every solution belongs to exactly one mesh. Mesh is a random effect because the numbered meshes are sampled realizations of the pipeline, not scientific conditions of interest. The subject and target are fixed.

## Slide 11
RANDOM-EFFECTS MODEL
The model separates between-mesh from within-mesh variation
TI repeatability • journal club
11
ONE OBSERVED ROI FIELD
observed field
=
overall mean
+
mesh-specific shift
+
repeat-to-repeat residual
yₘᵣ = μ + uₘ + εₘᵣ
BETWEEN MESHES • MESH VARIANCE
Do independently generated geometries give different average fields?
1 Average the 40 solutions within each mesh
2 Compare the 40 mesh means
Large value → remeshing changes the estimated field
WITHIN A MESH • RESIDUAL VARIANCE
If geometry is fixed, how much do repeated solutions still differ?
1 Compare each solution with its own mesh mean
2 Pool the remaining within-mesh scatter
Small value → the same mesh solves reproducibly
Total technical variance = mesh variance + within-mesh variance • mesh share = mesh variance / total
Scope: one fixed participant and target. The model attributes technical variation; it does not estimate population variance.
m = mesh • r = repeated solution • uₘ = mesh effect • εₘᵣ = residual within that mesh
Notes: Read the equation in plain language: an observed field is the overall mean plus the shift associated with that mesh plus residual repeat-to-repeat variation. The left component is estimated from the spread of mesh means. The right component is estimated from scatter around each mesh's own mean. Because there is one fixed participant and target, this is source attribution within this workflow, not population inference.

## Slide 12
RESULT 4 • FULLY NESTED SUBJECT
The nested case assigns virtually all observed variance to mesh generation
TI repeatability • journal club
12
Boundary: one participant • one target • one workflow. Source attribution, not population prevalence.
Between-mesh CV 2.018% • within-mesh CV 0.0040% • SD ratio 501×
Notes: Each point is the CV across 40 repeated solutions on one mesh. Most are exactly or effectively zero. The dashed line is the pooled within-mesh CV.
The between-mesh CV is 2.018%; pooled within-mesh CV is 0.0040%. The component SD ratio is 501-fold, and 99.9996% of total observed variance is attributed to mesh generation.
Keep saying 'in this participant' and 'in this workflow.'

## Slide 13
SENSITIVITY • FIXED MNI152 MODEL
Version sensitivity is systematic in amplitude—not spatial pattern
TI repeatability • journal club
13
4 / 4
ROIs lower under SimNIBS 4.0.1
−1.13% to −2.97%
change in mean field, 4.0.1 versus 4.5.0
r ≥ 0.99983
whole-brain voxelwise agreement
One fixed model: software sensitivity, not participant-level repeatability.
Fixed mesh, reference image, montage, ROI definitions, conductivities, and currents; runtime version changed
Notes: This is a separate sensitivity analysis on one fixed MNI152 model. The mesh, reference image, ROI definitions, montages, conductivities, currents, and electrode geometry were held constant; only the SimNIBS runtime version changed.
SimNIBS 4.0.1 produced a lower mean ROI field than 4.5.0 in all 4 ROIs. The relative shift ranged from −1.13% to −2.97%. Whole-brain spatial agreement remained extremely high, with Pearson r at least 0.99983; relative L2 differences ranged from 0.82% to 3.54%.
The interpretation is a small, systematic amplitude shift with the spatial pattern largely preserved. Do not pool this fixed-model version comparison with the participant or remeshing distributions, and do not attach population inference to the four ROIs.

## Slide 14
INTERPRETATION
Within-version evidence converges on mesh realization
TI repeatability • journal club
14
1
Cohort contrast
Remesh repeats spread; fixed-mesh repeats collapse across 10 participants and two targets.
2
Nested decomposition
Between-mesh SD is 501× the residual within-mesh SD in the fully nested subject.
3
Structural correlates
Element count and tissue-volume composition change across remesh realizations.
Inference: mesh realization is a numerical experimental factor and belongs in the uncertainty budget.
Dominant source of repeated-run variation ≠ proof that the selected mesh is the most accurate anatomy.
Evidence triangulation across field, variance, and mesh outcomes
Notes: The conclusion does not rest on a single plot. The main cohort shows the condition contrast, the nested experiment attributes the variance source, and structural metrics show that remeshing creates different numerical head models.
This is evidence that mesh realization is part of the computational specification. It is not evidence that any one realization is anatomically truer.

## Slide 15
IMPLICATIONS
The practical response depends on the scientific comparison
TI repeatability • journal club
15
Controlled contrasts
Freeze and checksum the mesh when comparing conditions within the same anatomy and meshing is a nuisance factor.
Percent-level effects
Repeat remeshing—or otherwise quantify discretization uncertainty—when the expected effect is similar to the observed CV.
Subject ranking
Avoid fine-grained selection or responder stratification from one mesh when participant means are close.
Reproducibility
Report meshing policy, selected-mesh provenance, software version, seed/selection rule, and remesh variability.
Rule of thumb for interpretation
If the scientific contrast is smaller than the mesh-induced spread, the mesh must enter the design or uncertainty statement.
Recommendations are scoped to the evaluated workflow
Notes: Mesh reuse is useful for controlled comparisons because it removes a nuisance source. It is not automatically the best strategy for absolute dosimetry or accuracy claims.
If the effect of interest is a few percent, either average or model multiple mesh realizations, or demonstrate empirically that mesh uncertainty is negligible relative to that contrast. Preserve and checksum the chosen mesh so the model can be reproduced.

## Slide 16
LIMITATIONS AND CLAIM BOUNDARIES
The result is strong about repeatability—and deliberately narrow about validity
TI repeatability • journal club
16
SUPPORTED
● Fresh remeshing introduces percent-level field variation in both evaluated targets.
● Repeated solving on one copied mesh is effectively deterministic.
● A single mesh can alter close between-subject rankings.
● The nested case isolates mesh generation as the dominant source for one participant.
NOT ESTABLISHED
● Which mesh is anatomically or physically most accurate.
● Generalization beyond 10 datasets, two targets, and this CHARM–SimNIBS pipeline.
● A specific tissue boundary or mesh metric as the causal mechanism.
● Population inference from the 1,600 nested technical observations.
Design caveat: the fixed mesh was selected using the primary outcome, so central agreement is partly imposed by design.
Technical repeats are not independent participants
Notes: The experiment is designed to quantify numerical repeatability, not validation against measured fields. Ten anatomical datasets and two targets provide replication, but not broad coverage of every montage or software stack.
The representative fixed mesh was selected using the primary field outcome, so its central value is expected to sit near the remesh center. The meaningful fixed-arm result is the near-zero spread conditional on that mesh—not independent accuracy.

## Slide 17
DISCUSSION
If the claim is smaller than the mesh noise, the mesh belongs in the claim
TI repeatability • journal club
17
1
Should future primary analyses average across mesh realizations—or standardize one mesh and treat it as part of the model definition?
2
What numerical-uncertainty threshold is acceptable before a simulated field difference is interpreted biologically?
3
Which extension adds the most value: more targets, another mesher, local boundary metrics, or convergence testing?
Take-home: a reproducible individualized field estimate requires specifying the mesh—not only the anatomy and montage.
Questions / critique / next experiment
Notes: Pause on the take-home sentence, then invite discussion. These questions are intentionally methodological: whether to average or standardize, how to set a numerical tolerance, and what experiment would most efficiently test generalization.

## Slide 18
BACKUP
Appendix • full ranking analysis: left hippocampus
TI repeatability • journal club
18
Exact pairwise probabilities + 20,000 one-repeat-per-participant draws
Notes: Use only if the audience wants to inspect which pairs drive ranking uncertainty.

## Slide 19
BACKUP
Appendix • full ranking analysis: right M1
TI repeatability • journal club
19
Exact pairwise probabilities + 20,000 one-repeat-per-participant draws
Notes: Use only if the audience wants to inspect which pairs drive ranking uncertainty.

## Slide 20
BACKUP
Appendix • cohort and stimulation parameters
TI repeatability • journal club
20
CamCAN cohort
ID
Recorded sex
Age
CC110174
Female
26.00
CC121144
Male
26.00
CC310407
Female
39.00
CC320616
Male
39.08
CC420071
Female
52.58
CC410432
Male
52.58
CC520083
Female
65.08
CC520127
Male
66.00
CC610631
Female
77.58
CC720941
Male
79.17
Target-specific TI montages
Target
Electrode pair
Current
Left hippocampus
F8–P8
2.000 mA
T7–P7
1.588656 mA
Right M1
Fp2–F6
2.000 mA
C4–CP2
0.632456 mA
Electrodes
20 × 20 × 2 mm circular in-plane • conductivity 1.4 S/m
Same participants evaluated for both target ROIs
Notes: The cohort is balanced by recorded sex and covers five age bands. Both target experiments use the same ten participants.

## Slide 21
PROVENANCE AND SENSITIVITY CHECKS
Appendix • the current results use the corrected spherical-ROI workflow
TI repeatability • journal club
21
Fixed-mesh selection correction
Historical selector
whole anatomical parcel median
Corrected selector
optimizer-matched spherical ROI median
18 / 20
participant–target representative meshes changed
Current deck uses the corrected fixed runs and unchanged historical remesh rows.
Finite-support sensitivity audit
97%
minimum finite ROI fraction • hippocampus
99%
minimum finite ROI fraction • M1
Within participant × condition correlations between finite support and field were weak:
hippocampus r = −0.074, ρ = −0.030
M1 r = 0.097, ρ = 0.063
Descriptive sensitivity check; not evidence of causality.
Analysis status: complete • 1,600 corrected cohort rows + 1,600 nested rows • source outputs read only
Analysis manifests dated 11 Sep 2026
Notes: The historical fixed mesh was selected using the anatomical parcel median, while the paper endpoint was refreshed to the optimizer-matched spherical ROI. Recomputing selection changed 18 of 20 participant–target representatives. The current presentation uses the regenerated spherical-fixed runs.
Some spherical ROI voxels were non-finite in a subset of runs, but support remained at least 97% in hippocampus and 99% in M1. Within-group correlations with the field metric were weak and are descriptive only.

## Slide 22
BACKUP
References and evidence sources
TI repeatability • journal club
22
1
Grossman N, et al. Noninvasive deep brain stimulation via temporally interfering electric fields. Cell. 2017;169:1029–1041.e16.
2
Rampersad S, et al. Prospects for transcranial temporal interference stimulation in humans: A computational study. NeuroImage. 2019;202:116124.
3
Windhoff M, Opitz A, Thielscher A. Electric field calculations in brain stimulation based on finite elements. Human Brain Mapping. 2013;34:923–935.
4
Saturnino GB, et al. SimNIBS 2.1: A comprehensive pipeline for individualized electric-field modelling. In: Brain and Human Body Modeling. 2019.
5
Puonti O, et al. Accurate and robust whole-head segmentation from MRI for individualized head modelling. NeuroImage. 2020;219:117044.
6
Indahlastari A, Chauhan M, Sadleir RJ. Benchmarking transcranial electrical-stimulation finite-element models. J Neural Eng. 2019;16:026019.
7
Shafto MA, et al. The Cambridge Centre for Ageing and Neuroscience study protocol. BMC Neurology. 2014;14:204.
Primary presentation evidence: corrected spherical-fixed and nested analysis manifests generated 11 September 2026.
Internal initial draft • source paths documented in build script
Notes: These references support the TI, SimNIBS, finite-element, and CamCAN context. The numerical results in the deck come from the corrected local analysis artifacts, not the older manuscript tables.